## Slide 1: Building An Eject-A-Bed
Jamie Dixon
Code Stock: 7/12/2014

## Slide 2: Material
Mattress
Metal-framed box spring
Used hospital bed
Erector Set
Servo
Netduino
Wifi Hub

## Slide 3: Get The Bed

## Slide 4: Figure Out How To Raise And Lower It
It runs on air – not electrical signals!

## Slide 5: Attach a servo to the bellow Attach the servo to the Netduino

## Slide 6: Add code to move the servo up and down
private static void ActivateServoForBellows()
{
uint period = 20000;
uint duration = 1500;
PWM servo = new PWM(PWMChannels.PWM_PIN_D5, period, duration, PWM.ScaleFactor.Microseconds, false);
servo.Start();
Thread.Sleep(2000);
InputPort button = new InputPort(Pins.ONBOARD_BTN, false, Port.ResistorMode.Disabled);
while (true)
{
if (button.Read())
{
servo.Duration = 1250;
Thread.Sleep(2000);
servo.Duration = 1500;
}
}
}

## Slide 7: Add code to move the servo up and down

## Slide 8: Add code to receive commands from a local browser
Make a socket
Set up web server
Listen for request
Get a request
Handle the request
  Move servo up/down
  Move servo back to TDC
Generate a response

## Slide 9: Add code to receive commands from a local browser

## Slide 10: Attach lift to frame

## Slide 11: Put it all together

## Slide 12: Intro To Netduino

## Slide 13: PWM

## Slide 14: Servo

## Slide 15: Questions?
jamessdixon@gmail.com
jamessdixon.wordpress.com
@jamie_dixon